Ms. Mindel De La Torre

Chief of the International Bureau

Federal Communications Commission

445 12th Street SW

Washington, DC  20554

Dear Ms. De La Torre:

The National Telecommunications and Information Administration (NTIA), on behalf of the Executive Branch agencies, approves the release of the draft Executive Branch proposal for WRC-15 which addresses agenda item 1.1 IMT stations operating in the adjacent band to Earth exploration-satellite service (1400-1427 MHz).

NTIA considered the federal agencies’ input toward the development of U.S. proposals for WRC-15.  NTIA forwards this package for your consideration and review by your WRC-15 Advisory Committee.  Mr. Charles Glass is the primary contact from my staff.

Sincerely,

(Original Signed April 1, 2015)

Paige R. Atkins

Associate Administrator

Office of Spectrum Management

UNITED STATES OF AMERICA

DRAFT PROPOSALS FOR THE WORK OF THE CONFERENCE

Agenda Item 1.1:  to consider additional spectrum allocations to the mobile service on a primary basis and identification of additional frequency bands for International Mobile Telecommunications (IMT) and related regulatory provisions, to facilitate the development of terrestrial mobile broadband applications, in accordance with Resolution 233 (WRC-12);

# Background Information:  NASA operates Earth exploration-satellite service (passive) sensors in the 1 400-1 427 MHz band.  The Aquarius passive sensor is currently flying on an Argentinian satellite, SAC-D.  NASA recently launched the Soil Moisture Active Passive (SMAP) satellite, which will begin operations in the near future.  SMAP carries a passive sensor that operates across the 1 400-1 427 MHz band.  Joint Task Group 4-5-6-7 completed compatibility studies regarding IMT and EESS (passive) in 1 400-1 427 MHz band that are contained in Report ITU-R RS.2336 jointly approved by ITU-R Study Group 7 and Study Group 5.  The draft CPM Report provides the following text regarding the summary of studies on unwanted emissions in the

# 1 400-1 427 MHz band:

“Draft new Report ITU-R RS.[EESS-IMT 1.4 GHz] (now Report ITU-R RS.2336) shows that, in order to protect EESS (passive) systems, the unwanted emission level of –60 dBW/27 MHz as currently recommended in Resolution 750 (Rev. WRC-12) is not sufficient and that the following levels of unwanted emissions in the 1 400-1 427 MHz frequency band are required:

For base stations:

–	−80 dBW/27 MHz in the case both 1 375-1 400 MHz and 1 427-1 452 MHz frequency bands are considered to be used simultaneously by IMT systems;

–	−75 dBW/27 MHz in the case only one of the 1 375-1 400 MHz or 1 427-1 452 MHz frequency bands is to be considered for IMT systems.

For user equipment:

# –	−65 dBW/27 MHz (This value is derived under the assumption that one UE is transmitting at an average output power of 15 dBm (over all resource blocks (RB)) per sector.  It would therefore have to be verified consistently according to these conditions.)

# To protect U.S. spaceborne assets operating in the 1 400-1 427 MHz band from potential harmful interference by IMT operations in the adjacent 1 427-1 518 MHz band, these OOBE limits are required for IMT and need to be made mandatory in the Radio Regulations.

Proposal:

MOD	USA/1.1/1

RESOLUTION 750 (Rev.WRC-15)

Compatibility between the Earth exploration-satellite service (passive) and relevant active services

…

TABLE 1-1

| EESS (passive) band | Active service band | Active service | Limits of unwanted emission power from active service stations in a specified bandwidth within the EESS (passive) band1 |
| --- | --- | --- | --- |
| 1 400 – 1427 MHz | 1 427 – 1452 MHz | Mobile | For IMT base stations: -75 dBW/27 MHz {Editor’s note: This may have to be revised if both bands around 1400 – 1427 MHz are used for IMT.} For IMT user equipment: -65dBW/27 MHz |
| 23.6-24.0 GHz | 22.55-23.55 GHz | Inter-satellite | −36 dBW in any 200 MHz of the EESS (passive) band for non-geostationary (non-GSO) inter-satellite service (ISS) systems for which complete advance publication information is received by the Bureau before 1 January 2020, and −46 dBW in any 200 MHz of the EESS (passive) band for non-GSO ISS systems for which complete advance publication information is received by the Bureau on or after 1 January 2020 |
| 31.3-31.5 GHz | 31-31.3 GHz | Fixed (excluding HAPS) | For stations brought into use after 1 January 2012: −38 dBW in any 100 MHz of the EESS (passive) band. This limit does not apply to stations that have been authorized prior to 1 January 2012 |
| 50.2-50.4 GHz | 49.7-50.2 GHz | Fixed-satellite (E-to-s)2 | For stations brought into use after the date of entry into force of the Final Acts of WRC-07: −10 dBW into the 200 MHz of the EESS (passive) band for earth stations having an antenna gain greater than or equal to 57 dBi −20 dBW into the 200 MHz of the EESS (passive) band for earth stations having an antenna gain less than 57 dBi |
| 50.2-50.4 GHz | 50.4-50.9 GHz | Fixed-satellite (E-to-s)2 | For stations brought into use after the date of entry into force of the Final Acts of WRC-07: −10 dBW into the 200 MHz of the EESS (passive) band for earth stations having an antenna gain greater than or equal to 57 dBi −20 dBW into the 200 MHz of the EESS (passive) band for earth stations having an antenna gain less than 57 dBi |
| 52.6-54.25 GHz | 51.4-52.6 GHz | Fixed | For stations brought into use after the date of entry into force of the Final Acts of WRC-07: −33 dBW in any 100 MHz of the EESS (passive) band |
| 1 The unwanted emission power level is the level measured at the antenna port. 2 The limits apply under clear-sky conditions. During fading conditions, the limits may be exceeded by earth stations when using uplink power control. TABLE 1-2 EESS (passive) band Active service band Active service Recommended maximum level of unwanted emission power from active service stations in a specified bandwidth within the EESS (passive) band1 1 400-1 427 MHz 1 350-1 400 MHz Radiolocation2 −29 dBW in the 27 MHz of the EESS (passive) band Fixed −45 dBW in the 27 MHz of the EESS (passive) band for point-to-point Mobile −60 dBW in the 27 MHz of the EESS (passive) band for mobile service stations except transportable radio-relay stations −45 dBW in the 27 MHz of the EESS (passive) band for transportable radio-relay stations 1 427-1 429 MHz Space operation (E-to-s) −36 dBW in the 27 MHz of the EESS (passive) band 1 427-1 429 MHz Mobile except aeronautical mobile −60 dBW in the 27 MHz of the EESS (passive) band for mobile service stations except IMT stations and transportable radio-relay stations3 −45 dBW in the 27 MHz of the EESS (passive) band for transportable radio-relay stations Fixed −45 dBW in the 27 MHz of the EESS (passive) band for point-to-point 1 429-1 452 MHz Mobile −60 dBW in the 27 MHz of the EESS (passive) band for mobile service stations except IMT stations and transportable radio-relay stations3 −45 dBW in the 27 MHz of the EESS (passive) band for transportable radio-relay stations −28 dBW in the 27 MHz of the EESS (passive) band for aeronautical telemetry stations4 Fixed −45 dBW in the 27 MHz of the EESS (passive) band for point-to-point 31.3-31.5 GHz 30.0-31.0 GHz Fixed-satellite (E-to-s)5 −9 dBW into the 200 MHz of the EESS (passive) band for earth stations having an antenna gain greater than or equal to 56 dBi −20 dBW into the 200 MHz of the EESS (passive) band for earth stations having an antenna gain less than 56 dBi 86-92 GHz6 81-86 GHz Fixed −41 − 14(f − 86) dBW/100 MHz for 86.05 ( f ( 87 GHz −55 dBW/100 MHz for 87 ( f ( 91.95 GHz where f is the centre frequency of the 100 MHz reference bandwidth expressed in GHz 92-94 GHz Fixed −41 − 14(92 − f) dBW/100 MHz for 91 ( f ( 91.95 GHz −55 dBW/100 MHz for 86.05 ( f ( 91 GHz where f is the centre frequency of the 100 MHz reference bandwidth expressed in GHz 1 The unwanted emission power level is the level measured at the antenna port. 2 The mean power is to be understood here as the total power measured at the antenna port (or an equivalent thereof) in the band 1 400-1 427 MHz, averaged over a period of the order of 5 s. 3 Stations of the mobile service for cellular systems, including those complying with Recommendation ITU-R M.1457or IMT standards, are likely to meet this unwanted emission power level. 4 The band 1 429-1 435 MHz is also allocated to the aeronautical mobile service in eight Region 1 administrations on a primary basis exclusively for the purposes of aeronautical telemetry within their national territory (No. 5.342). 5 The recommended maximum levels apply under clear-sky conditions. During fading conditions, these levels may be exceeded by earth stations when using uplink power control. 6 Other maximum unwanted emission levels may be developed based on different scenarios provided in Report ITU-R F.2239 for the band 86-92 GHz. |

Reasons:  Appropriate unwanted emission limits are required to protect EESS passive systems operating in the band 1 400-1 427 MHz from IMT stations operating in the adjacent band. Canada is currently assessing the impact of the new limits.  As such, in the proposal above, the unwanted emission limits contained in Report ITU-R RS-2336 are shown in square brackets.

MOD	USA/1.1/2

5.338A	In the bands 1 350-1 400 MHz, 1 427-1 452 MHz, 22.55-23.55 GHz, 30-31.3 GHz, 49.7-50.2 GHz, 50.4-50.9 GHz, 51.4-52.6 GHz, 81-86 GHz and 92-94 GHz, Resolution 750 (Rev.WRC-15) applies.    (WRC-15)

[NOTE:  consequential changes to the Table of Allocations will also be required.]

Reasons:  The changes to the references in No. 5.338A are consequential to the revision of Resolution 750.

______________